| NO. | HX-RS-SMTP02 |
| --- | --- |
| NAME | Surface mount type platinum resistance temperature sensor |
| FEATURES | Temperature measurement for the surface of an object or equipment. |
| DESCRIPTION | 1.Products comply with IEC751 and EN60751 related standards. 2.Products designed to meet the provisions of the temperature sensor. 3.Components:Pt100. 4.Resistance:100Ω,at 0℃. 5.Accuracy: Class A,±（0.15+0.002*¦T¦）℃. 6.R/R ratio(ohm/ohm/℃):0.003851. 7.Working current:≤1mA. 8.insulating resistance:≥100MΩ. 9. Insulation voltage:≤500VDC. 10. Temperature range:-50～200℃(Or customer specified). 11. Size: 8*7.6*2.2mm . 12. Sensor structure: Single type. 13. Lead: 2wire,L=13mm. 14. Material:Cu. 15.Pressure: 0.6MPa. 16. Installation: Paste. 17. Measurement object: For measuring a flat surface. 18. Seal: IP68.Mechanical suppression. |
| ACCURACY AND RESISTANCE FOR TEMPERATURE |
| Temperature(℃) -50 0 100 200 Resistance(Ω) 80.31 100 138.51 175.86 Accuracy(℃) ±0.25 ±0.15 ±0.35 ±0.55 |
| ELECTRICAL CONNECTIONS |
| 2-wire |
| PHYSICAL SAMPLE |
| DRAWING |
| HX-RS-SMTP02 |
| Product selection |
| Model | Code | Parameter | Note |
| HX-RS-SMTP02 | P | Pt100 |  |
| Accuracy | A | Class A |  |
|  | B | Class B |  |
| Temperature range | 1 | -20～85℃ |  |
|  | 2 | -50～150℃ |  |
|  | 3 | -50～200℃ |  |
|  | 4 | Customer designation |  |
| Lead | Structure | 2 | 2-Wire |  |

# Text boxes

Pt100

Pt100